## Slide 1
Comparison of building occupants activities detection methods using simulated data: a case of window opening detection
CHUHAO JIANG and MARIE-LISE PANNIER and ALAIN GODON and DAVID BIGAUD
Conférence Francophone de l'International Building Performance Simulation Association
| 19-20 May 2022, Châlons-en-Champagne, France
- 19.05.2022
Chuhao Jiang
PhD student
Notes: Hello Professor Monika, professor Stephane, professor David, professor marie, my name is Chuhao Jiang, and I come from China, I obtain my master of science degree from technical university of Denmark which is located in Copenhagen, Denmark. I am currently a first year Phd student in university of angers, This is my first CSI presentation for my thesis

## Slide 2: Introduction
Development of smart buildings
Minimisation of energy consumption
Maximisation of occupants’ comfort
Need to understand occupants’ behaviour :
  Presence / Absence
  Activities : windows openings, …
  Thermal preferences
Use of data-driven methods
Preferences
Advices
Sensors
Actuators
Actions
State
Toward a user-centric energy management for smart buildings
Introduction Case study Methodology Results Conclusion
Notes: Nowadays, building is biggest energy consumption sector in the world, we can see from left figure, almost 40 percent energy consumed by building
a reasonable balancing between the human and smart building must be found. So we want input a user centric optimization which combine user location, activity and so on as user info to smart building operation phase to achieve the comfort conditions for occupants

## Slide 3: Introduction
Data-driven methods for presence and activity detection, according to the literature :
  Supervised methods mostly used
  e.g. : logistic regression for windows openings
Practical application of supervised methods ?
  Need of many labelled data !
Review of Xilei et al., 2020
Use of machine learning methods for the detection of windows openings
Unsupervised
Supervised
Semi-supervised
Logistic regression
Markov Chain / Hidden Markov Chain
Linear / Non-linear regression
ANN
Bayesian
Random forest
SVM
Gauss regression
Introduction Case study Methodology Results Conclusion
Notes: Data source: Xilei Dai, Junjie Liu, Xin Zhang. 2020. “A review of studies applying machine learning models to predict occupancy and window-opening behaviours in smart buildings“
supervised machine learning work well and have been successfully used in the literature, but how to deal with non labelled data? + goal of the article is to compare the performance of different ML methods on the detection of windows openings

## Slide 4: Case study
Application of
unsupervised, supervised and semi-supervised methods for the detection of windows openings on simulated data
Introduction Case study Methodology Results Conclusion
Selected features :
  Indoor temperature
  Outdoor temperature
  Solar gains
  Occupants heat gains
  Computers heat gains
  Heating power
  Windows status : to predict
Simulation of 1 year for a computer lecture room with DesignBuilder
Random generation of 15 min openings at business hours
Few openings during the year : highly imbalanced data
Notes: In absence of measured data, a simulated highly imbalanced data are used to test the performance of ML windows detection methods
window opening can only occur between 8 a.m. to 7 p.m. on the weekdays, window status can change every 15 minutes, and window remains open up to 30 minutes

## Slide 5: Methodology
Introduction Case study Methodology Results Conclusion
Notes: TP (True Positive): the case is positive, and it has been detected as positive;
FP (False Positive): the case is negative, and it has been detected as positive;
TN (True Negative): the case is negative, and it has been detected as negative;
FN (False Negative): the case is positive, and it has been detected as

## Slide 6: Methodology
Introduction Case study Methodology Results Conclusion
Time dd/jj hh:mm:ss | Indoor temp. | Outoor temp. | Solar gains | Occ. gains | Comp. gains | Heat. power | Win. status
dd/jj hh:mm:ss | 12.3 °C | 12.3 °C | 1,500 W | 800 W | 1,200 W | 400 W | closed
dd/jj hh:mm:ss | 12.3 °C | 12.3 °C | 1,500 W | 800 W | 1,200 W | 400 W | closed
dd/jj hh:mm:ss | 12.3 °C | 12.3 °C | 1,500 W | 800 W | 1,200 W | 400 W | closed
… | … | … | … | … | … | … | …
dd/jj hh:mm:ss | 12.3 °C | 12.3 °C | 1,500 W | 800 W | 1,200 W | 600 W | opened
dd/jj hh:mm:ss | 12.3 °C | 12.3 °C | 1,500 W | 800 W | 1,200 W | 400 W | closed
dd/jj hh:mm:ss | 12.3 °C | 12.3 °C | 1,500 W | 800 W | 1,200 W | 400 W | closed
Input
Output to predict
x % training
(100-x) % testing
Database
Notes: TP (True Positive): the case is positive, and it has been detected as positive;
FP (False Positive): the case is negative, and it has been detected as positive;
TN (True Negative): the case is negative, and it has been detected as negative;
FN (False Negative): the case is positive, and it has been detected as

## Slide 7: Methodology
Multivariate Gaussian distribution:
Fit model by setting ，
Calculate probability density for a new sample
Set the threshold
Principal Component Analysis (PCA):
Reconstruction the data
Calculate the reconstruction error
Set the threshold
Introduction Case study Methodology Results Conclusion
Unsupervised
x % training
(100-x) % testing
Notes: TP (True Positive): the case is positive, and it has been detected as positive;
FP (False Positive): the case is negative, and it has been detected as positive;
TN (True Negative): the case is negative, and it has been detected as negative;
FN (False Negative): the case is positive, and it has been detected as

## Slide 8: Methodology
Introduction Case study Methodology Results Conclusion
Much more « closed » than « opened » : imbalanced data
Supervised
x % training
(100-x) % testing
Notes: Random oversampling involves randomly selecting examples from the minority class, with replacement, and adding them to the training dataset. Random undersampling involves randomly selecting examples from the majority class and deleting them from the training dataset.

## Slide 9: Methodology
AutoEncoder:
Train the AE with Normal data
Put new data into AE
Compare the reconstruction error of new data with normal data
Introduction Case study Methodology Results Conclusion
Semi-supervised
x % training only on « closed » data
(100-x) % testing on both « closed » and « opened » data
Notes: TP (True Positive): the case is positive, and it has been detected as positive;
FP (False Positive): the case is negative, and it has been detected as positive;
TN (True Negative): the case is negative, and it has been detected as negative;
FN (False Negative): the case is positive, and it has been detected as

## Slide 10: Methodology
Confusion matrix |  | Prediction | 
 |  | Window closed | Window opened
Reality | Window closed | True negative (TN) | False positive (FP)
 | Window opened | False negative (FN) | True positive (TP)
Introduction Case study Methodology Results Conclusion
Performance assessment
Maximise recall
Notes: TP (True Positive): the case is positive, and it has been detected as positive;
FP (False Positive): the case is negative, and it has been detected as positive;
TN (True Negative): the case is negative, and it has been detected as negative;
FN (False Negative): the case is positive, and it has been detected as

## Slide 11: Methodology
Introduction Case study Methodology Results Conclusion
Choice of the methods
 | Unsupervised |  | Supervised | Semi-supervised
 | Multivariate Gaussian distribution | Principal Component Analysis (PCA) | Logistic regression | AutoEncoder
Reason why applying the methods | Robust model for data following a Gaussian distribution Consider the correlation of features | Traditional method No data distribution assumption Decorrelate relationship between variables | Widely used methodology Efficient for two classes classification tasks | Successfully applied in fault detection context No loss of information by dimensionality reduction
Notes: TP (True Positive): the case is positive, and it has been detected as positive;
FP (False Positive): the case is negative, and it has been detected as positive;
TN (True Negative): the case is negative, and it has been detected as negative;
FN (False Negative): the case is positive, and it has been detected as

## Slide 12: Results
Confusion matrix |  | Prediction | 
 |  | Window closed | Window opened
Reality | Window closed | 10,474 | 0
 | Window opened | 10 | 28
Introduction Case study Methodology Results Conclusion
Supervised method without under- or over-sampling
(Method used in the literature)
Notes: TP (True Positive): the case is positive, and it has been detected as positive;
FP (False Positive): the case is negative, and it has been detected as positive;
TN (True Negative): the case is negative, and it has been detected as negative;
FN (False Negative): the case is positive, and it has been detected as

## Slide 13: Results
 | Unsupervised |  | Supervised |  |  | Semi-supervised
 | Multivariate Gaussian distribution | Principal Component Analysis | Logistic regression Baseline | Logistic regression Undersampling | Logistic regression Oversampling | AutoEncoder
Precision | 32 % | 7 % | 100 % | 100 % | 100 % | 100 %
Recall | 88 % | 81 % | 73 % | 100 % | 97 % | 75 %
Introduction Case study Methodology Results Conclusion
All methods
Notes: TP (True Positive): the case is positive, and it has been detected as positive;
FP (False Positive): the case is negative, and it has been detected as positive;
TN (True Negative): the case is negative, and it has been detected as negative;
FN (False Negative): the case is positive, and it has been detected as

## Slide 14: Conclusions and Perspectives
Introduction Case study Methodology Results Conclusion
Comparison of the performances of methods to detect windows openings using simulated data
Supervised methods performed better … … but may be difficult to apply in practice (labelling)
Semi-supervised methods : promising method
More realistic openings scenarios
Study of the effect of seasonality
Detect and distinguish between different events : opening + change in occupancy
Toward measured data in real classrooms
Notes: 1. the supervised method performs better than the others. However, it has disadvantages.
2. the semi-supervised method has good precision and recall. As it requires little labelled data, it could be a satisfactory solution for the detection of occupant behaviour.
labelling all the data is time consuming and resource intensive
it is not applicable in the real world. For the unsupervised approach
1.A more realistic simulated opening scenario will be generated, and the seasonality effect will be analysed.
2. Then, real data collected in classrooms will be investigated with these methods. Sensors have been installed in the polytech building of University Angers.
3. A challenge in the detection process will be to distinguish if the outliers are due to windows events or to a change in the occupancy rate.

## Slide 15
RFI Wise BI T
Notes: Ritto et al [60]. proposed an improvement of the effective independence method, which uses the effective independence method to the proper orthogonal modes of a non-linear system. In this way, the response of non-linear system is reduced to the modal participation factors of a linear structure, and the modal transformation can be treated as a projection of the non-linear response onto the subspace spanned by the mode shapes of the linear system.