## Slide 1
Assessment of multiple advanced Bayesian calibration algorithms in building energy models
Le 19 / Mai /2022
Presented by: Samih Akkari
Thesis director: Bruno Peuportier
Thesis master: Patrick Schalbart

## Slide 2
Applications
Retrofit existing buildings
Energy performance guarantee
What is calibration?
It is the process of adjusting model parameters to fit to data
Presentation content:
Present calibration methodology
Application on a case study
Compare different calibration methods
Context
1 / 9
Why calibrate the model?
Uncertain/unknown model parameters

## Slide 3
Presentation plan
2 / 9
Sensitivity analysis
Calibration methods
Selection of the methods from literature
Case study
Presentation of the case study
Selection of most important parameters
Application/comparison of selected calibration methods
Conclusion

## Slide 4
Sensitivity analysis (SA)
Importance of calibrating a subset of the parameters
Avoid over-parametrisation
Reduce the computational cost
3 / 9
Sensitivity analysis
Quantifies the influence of each parameter on the model output
Sensitivity methods
Local methods
Screening methods
Variance-based methods
  Sobol method is used

## Slide 5
Calibration algorithms
Approximate Bayesian computation (ABC) |  | Kennedy O’Hagan framework (KOH) Sampling techniques
Population Monte Carlo (ABC-PMC) |  | Metropolis Hastings
Adaptive ABC (aABC-PMC) |  | Adaptive transitional (CATMIP)
Simulated annealing (SABC) |  | No-U-turn (NUTS)
Random forest (ABC-RF) |  | Adams
Adaptive PMC (APMC) |  | 
Families of Bayesian inference
4 / 9

## Slide 6
Case study
IBB-house, INCAS platform (Le Bourget du Lac)
 |  | Scenario 1 |  | Scenario 2 |  | Scenario 3 |  | Scenario 4 |  | Scenario 5 |  | Scenario 6 |  | 
Heating power |  | 20˚C |  | Off |  | Off |  | 24˚C |  | Off |  | Off |  | 
Ventilation mode |  | BP |  | Off |  | Off |  | BP |  | BP |  | BP |  | 
Ventilation flow rate |  | Rate-a |  | 0 |  | 0 |  | Rate-a |  | Rate-a |  | Rate-b |  | 
Shutters |  | Closed |  | Closed |  | Closed |  | Closed |  | Open |  | Open |  | 
 | 01/01/2012 | 16/01/2012 | 16/01/2012 | 09/02/2012 | 09/02/2012 | 20/02/2012 | 20/02/2012 | 15/03/2012 | 15/03/2012 | 31/03/2012 | 31/03/2012 | 22/04/2012 | 22/04/2012 | 
5 / 9
Model comprise 113 parameters |  |  | 
Model parameters | Selected probability distributions |  | 
 | Type | Mean | Standard deviation
Ventilation () | Normal | 110 | 11
Dissipated heat (W) | Normal | 208 | 20.8
Polystyrene conductivity (W/m.K) | Normal | 0.03 | 0.003
… | … | … | …
Model comprise 113 parameters |  |  | 
Model parameters | Selected probability distributions |  | 
 | Type | Mean | Standard deviation
 | Normal | 110 | 11
Dissipated heat (W) | Normal | 208 | 20.8
Polystyrene conductivity (W/m.K) | Normal | 0.03 | 0.003
… | … | … | …
Description of the case study

## Slide 7
Controlled conditions
6 / 9
Chart: Parameters
| Ventilation flowrate | Heating power | Specific heat concrete wall | Conductivity polystyrene wall | Heat dissipated | Albedo | Specific heat concrete Screed | Conductivity polystyrene Styrofoam
 | 0.54909 | 0.32448 | 0.20023 | 0.16335 | 0.085665 | 0.083076 | 0.036769 | 0.035555
This graph shows the most important parameters ranking via Sobol method

## Slide 8
Real data
This graph shows the model predictive performance of each method with simulation budget of 44,000
7 / 9
Chart: Scenarios
| 1 (training) | 2 (training) | 3 (training) | 4 (testing) | 5 (training) | 6 (testing)
APMC | 0.19357 | 0.17135 | 0.12813 | 0.45264 | 0.39142 | 0.25084
ABC-PMC | 0.23354 | 0.25695 | 0.24809 | 0.60263 | 0.44962 | 0.30312
CATMIP | 0.21424 | 0.19432 | 0.18288 | 0.59245 | 0.43278 | 0.29696
Adams | 0.19904 | 0.16901 | 0.14859 | 0.48799 | 0.39615 | 0.26698
RF | 0.36641 | 0.38734 | 0.3281 | 0.38899 | 0.65128 | 0.46215
Priors | 0.71956 | 1.2676 | 1.3146 | 1.0807 | 0.70972 | 0.58478
APMC fits best to data while RF fits the worst

## Slide 9
Real data
This graph shows the model predictive performance of each method with increasing number of model evaluations
8 / 9
Variability in RF but potential with less number of model evaluations
RF does not reach similar accuracy even with 100000 simulations
All algorithm converge to better accuracy with more number of simulations except RF

## Slide 10
Conclusion and perspective
Achieved work presented
Calibration of a case study with recent methods
Evaluation of the accuracy and computational efficiency of different methods
RF if approximate results are needed with limited simulations
For more accurate results other algorithms are preferred
Perspective
Investigating more the robustness and accuracy of RF with limited simulations
9 / 9

## Slide 11
BABA Loubna – 13/ Janvier / 2020
Thank you
for your attention

## Slide 12
Model predictive performance
Chart: 
Chart: 
Hours
Hours
T°C
Monozone model is not able to replicate the variability in temperature profile occurring in zone 5
T°C
Temperature profile (scenario_5)
Temperature profile (all scenarios)